## Slide 1
Slim and self-adjusting
Round cylinders DSNU, ESNU and DSNU-S

## Slide 2: Slim and self-adjusting
Round cylinders DSNU, ESNU and DSNU-S
DSNU
(ISO)
(ISO)
DSNU-S-...
 8 ... 16
DSNU-S-...
 20/25

## Slide 3: Slim and self-adjusting
Round cylinders DSNU, ESNU and DSNU-S
Agenda:
Brief overview of the drive
Find out about solutions for your requirements
DSNU
(ISO)
(ISO)
DSNU-S-...
 8 ... 16
DSNU-S-...
 20/25

## Slide 4: Slim and self-adjusting
Round cylinders DSNU, ESNU and DSNU-S
Best performance proven reliability of the DSNU, ESNU series
Extremely versatile thanks to optional variants in the modular system for the DSNU, ESNU
Minimal space requirement New space-optimised series DSNU-S
Extremely easy and time-saving installation With self-adjusting cushioning PPS
Extremely economical Thanks to attractive price and long service life
Easily available Short delivery times and worldwide availability of the Core Range
DSNU
(ISO)
(ISO)
DSNU-S-...
 8 ... 16
DSNU-S-...
 20/25

## Slide 5: Pneumatic round cylinder
DSNU, ESNU (ISO)
DSNU-S (space-saving)
For use in any application, standardised (ISO 6432)
Reliable design principles for over 30 years
Wide range of applications and variants
Up to 35 mm shorter
Up to -40% slimmer
Designed for direct mounting in space-critical applications
Update
2021
Since July 2020

## Slide 6: DSNU, ESNU ISO variants – Product relaunch
Updates from 2021
Continuation of usual part numbers and type codes
Spanner flats
for easy installation
Tried-and-tested materials
Piston, piston rod, seals, bearings, grease
 Dimensional changes
Label with Product Key
Permanent digital product identification
Polymer bearing for pivoting
Smooth running and low wear
Same technical features
Same mounting surfaces
PUR seals
Low wear
Sensing option using the new self-adjusting proximity sensor SDBT-MSX with auto teach-in function

## Slide 7: New possibilities of the space-saving DSNU-S
Smallest space requirements for your machine design
Up to 40% slimmer
Up to 35 mm shorter than DSNU ISO variants
 Unbeatable in tight conditions
Lightweight
Easy to assemble, even when things are tight
Self-adjusting cushioning above Ø 16
Self-adjusting proximity sensor SDBT-MSX
 It doesn’t get any faster
Optimised dimensions DSNU-S
Proximity sensor SDBT-MSX with auto teach-in
Self-adjusting
pneumatic cushioning PPS
Copper-free variant available
Usage for battery production

## Slide 8
Your
requirements?
Availability
Features
Product service life
Applications
Functions
Maintenance
Warehousing
Tips and tricks
Delivery time

## Slide 9: Topics
DSNU
(ISO)
DSNU-S-...
 8 ... 16
DSNU-S-...
 20/25
Motivation
Features
Dimensions
Interfaces
Sustainability
Application
Features
Dimensions
Technical data
Comparison:
Accessories
Features
Overview
PPS cushioning
Forces

## Slide 10: Features
DSNU (ISO)
Seal for piston rod and piston made of PUR
Wear resistant
Economical by long lifetime
Barrel made of stainless steel
Sturdy design
Economical by long lifetime
Piston with integrated elastic cushioning element
Standard with all cushioning variants
Reduced effort for noise reduction
Robust for max. impact force
High performance also with higher loads and speeds
Economical by long lifetime
Self-adjusting pneumatic cushioning PPS
Easy installation
Time saving
Reduced space requirements w/o screw
Tamper-proof
Label with product-key
Unique product identification
Service for customer and logistics, re-ordering and traceability
Rod bearing made of sintered metal
Robust performance with lateral loads, long strokes and applied moment with pivoting
Economical by long lifetime
Polymer bearing for pivoting
Standard for all sizes
Reduced wear
Economical by long lifetime
Variety of optional modular kit types
Perfect fit to the surroundings
Easy ordering of serial products
Global availability by known order channels
Piston with magnet for sensing standard
Easy product selection and stock handling
Usage of new self-adjusting cylinder switch SDBT-MSX
Piston rod made of stainless steel
Corrosion and wear resistant to prevent leakage
Economical by long lifetime

## Slide 11: Dimensions
Compatibility comparison
Ø | 8 | 10 | 12 | 16 | 20 | 25 | 32 | 40 | 8 | 10 | 12 | 16 | 20 | 25 | 32 | 40
AM | 12 |  | 16 |  | 20 | 22 | 22 | 24 | 12 |  | 16 |  | 20 | 22 | 22 | 24
WF | 16 |  | 22 |  | 24 | 28 | 34 | 39 | 16 |  | 22 |  | 24 | 28 | 34 | 39
BF | 12 |  | 17 |  | 20 | 22 | 26 | 30 | 12 |  | 17 |  | 20 | 22 | 26 | 30
H | 28 |  | 38 |  | 44 | 50 | 56 | 63 | 28 |  | 38 |  | 44 | 50 | 56 | 63
L2+ | 46 |  | 50 | 56 | 68 | 69.5 | 69.5 | 84.6 | 46 |  | 50 | 56 | 68 | 69.5 | 69.5 | 84.6
ZJ+ | 62 |  | 72 | 78 | 92 | 97.5 | 103.5 | 123.6 | 62 |  | 72 | 78 | 92 | 97.5 | 103.5 | 123.6
XC+ | 64 |  | 75 | 82 | 95 | 104 | 117.5 | 139.6 | 64 |  | 75 | 82 | 95 | 104 | 117.5 | 139.6
D1 | 15 |  | 20 |  | 27 | 27 | 38 | 46 | 14 |  | 18 |  | 26 | 27 | 38 | 45
D | 15 |  | 20 |  | 27 |  | 38 | 46 | 16 |  | 20 |  | 30 |  | 41 | 49
KV | 19 |  | 24 |  | 32 | 32 |  |  | 19 |  | 24 |  | 32 | 32 |  | 
KK | M4 |  | M6 |  | M8 | M10 x1.25 | M10 x1.25 | M12 x1.25 | M4 |  | M6 |  | M8 | M10 x1.25 | M10 x1.25 | M12 x1.25
BE | M12x1.25 |  | M16x1.5 |  | M22x1.5 |  | M30 x1.5 | M38 x1.5 | M12x1.25 |  | M16x1.5 |  | M22x1.5 |  | M30 x1.5 | M38 x1.5
EE | M5 |  |  |  | G1/8 |  |  | G1/4 | M5 |  |  |  | G1/8 |  |  | G1/4
-P | 5,5 |  | 7 |  | 9,5 | 8,5 | 13 | 15 | 5 |  | 6 |  | 9 | 8,5 | 13 | 14,5
DSNU (old)
DSNU (ISO)
H
Height D1
Width D1
Diagonal
Ø D
Max. depth of air supply connection (-P)

## Slide 12: Applications
Deltas in the space required for the new design
Comparison of end caps DSNU (ISO)
Ø | Width = Height = D1 | Diagonal D | Max. depth of air supply connection | Design
8 | - 1 mm | + 1 mm | - 0,5 mm | New design
10 | - 1 mm | + 1 mm | - 0,5 mm | 
12 | - 2 mm | 0 | - 1 mm | 
16 | - 2 mm | 0 | - 1 mm | 
20 | - 1 mm | + 3 mm | - 0,5 mm | 
25 | 0 | + 3 mm | 0 | 
32 | 0 | + 3 mm | 0 | 
40 | - 1 mm | + 3 mm | - 0,5 mm | 
50 | 0 | 0 | 0 | Old design
63 | 0 | 0 | 0 | 
Height
Width
Diagonal
= height
Width = diagonal
Max. depth
Air supply connection
DSNU (ISO)
Old DSNU

## Slide 13: Motivation
Space-optimised design
Attractively priced
Extended portfolio for round cylinders
DSNU-S-...

## Slide 14: Features
DSNU-S-... space optimized
Barrel made of stainless steel
Sturdy design
Economical by long lifetime
Piston with magnet for sensing standard
Easy product selection and stock handling
Usage of new self-adjusting cylinder switch SDBT-MSX
Piston with integrated elastic cushioning element
Standard with all cushioning variants
Reduced effort for noise reduction
Robust for max. impact force
High performance also with higher loads and speeds
Economical by long lifetime
Label with product-key
Unique product identification
Service for customer and logistics, re-ordering and traceability
Without separate piston rod bearing
Slim design for mounting thread at bearing cap
Economical by minimized space requirement
Free of copper
Usage for battery production
No emisson of unwanted particles
Quality of production
Self-adjusting pneumatic cushioning PPS
Easy installation
Time saving
Reduced space requirements w/o screw
Tamper-proof
Piston rod made of stainless steel
Corrosion and wear resistant to prevent leakage
Economical by long lifetime
Without pivot bearing and without mounting thread for bore size 8/12/16
Short end cap
Economical by minimized space requirement
Seal for piston rod and piston made of PUR
Wear resistant
Economical by long lifetime

## Slide 15: The new way of saving space with the DSNU-S
Up to 35 mm shorter
Up to 40%
slimmer
DSNU to ISO 6432
Standardised interfaces for easy connection
Wide range of variants for greater flexibility
DSNU-S space-saving
For tight installation spaces
Enables a sustainable machine design and an energy-saving layout for handling units
Same nominal diameter and stroke length
Shown here: DSNU/-S-16-25-P-A

## Slide 16: Application example for parallel mounting
DSNU-S space-saving
Parallel mounting for separating workpieces at buffer sections
Features:
For simple linear movements
For small to medium strokes
For low transverse loads
For handling small workpieces
For limited installation space in terms of width (mounted in parallel)
Video @ Content Hub #144896

## Slide 17: Pneumatic round cylinder for durable and compact machine design
Up to 50% lighter
Reduced weight
Lower moving mass
Energy-efficient handling

## Slide 18: An interface for every eventuality
Simply part of the solution
DSNU-S-...
with multiple interfaces
Piston rod thread
K2 – extended
K6 – shortened
K3 – with female thread
Piston rod
K8 – extended
K2
K6
End cap
MQ - short with
lateral supply port
MA - with axial supply port
MX - with
mounting thread
MP - with swivelling rod eye
MQ
MA
MX
MP
K3
K8

## Slide 19: DSNU, ESNU ISO types
Square piston rod (protection against rotation)
Through piston rod
Heat-resistant seals up to 120 °C
Corrosion resistant with NSF-H1 grease
From 2021: FPM seal for increased chemical resistance
Extended male piston rod thread
Female piston rod thread
Special thread on the piston rod
Piston rod with male thread shortened at one end
Extended piston rod
From 2021: Low friction
Constant motion (at low piston speeds)
Clamping unit on the piston rod
ATEX II 2GD compliant
Dust protection (seal with scraper) 32… 63 mm
Metal scraper 32 … 63 mm
ESNU single-acting
Wide choice of variants and features
MH
Direct mounting on the bearing cap
Short end cap with lateral supply port
MQ
Short cylinder end cap
with lateral supply port
MA
Axial
supply port
Standard

## Slide 20: Sustainable development
Less material consumption
Less weight
Less space required
More compact designs
Conserving resources
Faster switching
Less moving weight
Easier to operate
Less storage space
More efficient warehousing
Simply part of our future range
DSNU-S-...
up to 35 mm shorter
up to 40% slimmer

## Slide 21: Dimensions
DSNU-S-... compared to DSNU (ISO)
Ø | 8 | 12 | 16 P | 16 PPS | 20 | 25 | 8 | 10 | 12 | 16 | 20 | 25
AM | 12 | 16 | 16 |  | 20 | 22 | 12 |  | 16 |  | 20 | 22
WF | 12 | 13 | 13 |  | 17 | 20 | 16 |  | 22 |  | 24 | 28
BF | 8 | 8 | 8 |  | 13 | 13 | 12 |  | 17 |  | 20 | 22
H | 24 | 29 | 29 |  | 37 | 42 | 28 |  | 38 |  | 44 | 50
L2+ | 45 | 46 | 46 | 57 | 58 | 61 | 46 |  | 50 | 56 | 68 | 69.5
ZJ+ | 58 | 59 | 60 | 70 | 76 | 81 | 62 |  | 72 | 78 | 92 | 97.5
D | 12 | 14 | 18 |  | 24 | 27 | 14 |  | 18 |  | 26 | 27
KV | 11 | 14 | 14 |  | 26 | 26 | 19 |  | 24 |  | 32 | 32
KK | M4 | M6 | M6 |  | M8 | M10 | M4 |  | M6 |  | M8 | M10
BE | M8 | M10 | M10 |  | M20 | M20 | M12x1.25 |  | M16x1.5 |  | M22x1.5 | 
EE | M5 |  |  |  | G1/8 |  | M5 |  |  |  | G1/8 | 
-P | 4 | 4 | 6 |  | 8 | 8,5 | 5 |  | 6 |  | 9 | 8,5
DSNU-S-...
DSNU (ISO)
Max. depth of air supply connection (-P)

## Slide 22: Forces
DSNU-16 (ISO)
DSNU-S-16
Allowable lateral load
Allowable lateral load

## Slide 23: Forces
DSNU-25 (ISO)
DSNU-S-25
Allowable lateral load
Allowable lateral load

## Slide 24: Technical data
General selection
DSNU-S-...
8/12/16/20/25
200 mm
200 mm
P/PPS
Standard
All Ø
For Ø 20/25
Not possible
Not possible
DSNU (ISO)
8/10/12/16/20/25/32/40/50/63
500 mm
500 mm (longer on request, up to 2,000 mm)
P/PPS/PPV
Standard
All Ø
All Ø
Incl. pivoting for all Ø
Available
Nominal size
Max. standard strokes
Max. intermediate strokes
Cushioning
Magnet for position measurement
Mounting thread on bearing cap
Mounting thread on end cap
Pivot device on end cap
Modular system variants

## Slide 25: Features
DSNU-S-... compared to new DSNU (ISO)
Even thinner
Caps about -3 mm more flat than new DSNU
Smaller mounting threads and nuts (up to -40%)
Same P and PPS cushioning
No PPV available
Shorter end caps
Without hole for swivel bearing
Ø 20/25 with threat as standard
Cylinder in total ~2,5 cm shorter than DSNU
DSNU-S-16-P 1 cm shorter than DSNU-S-16-PPS
DSNU-S-20/25-P same length as -PPS
Less space requirement with focused usage on direct mounting
Air supply port
Same types M5 and G1/8
~1mm less deep
Ø 20/25-PPS
Without separate bearing
Free of copper
Reduced max. lateral load
Smaller mounting threat size for min. total width
Same PUR piston rod seal
Ø 8…16 behind bearing
Ø 20/25 in front of bearing
Same piston rod
Stainless steel
Same piston
Magnet and elastic damping standard
Same max. energy
Same grease
PWIS free
Same barrel
Stainless steel
Available sizes
Ø 8, 12, 16, 20, 25
Without Ø 10
Same material for end caps
Anodized aluminium
Same rolling connection
Same look
Different mounting interfaces
Smaller threads
Not interchangeable

## Slide 26: Simply better with self-adjusting cushioning PPS
Effective pneumatic cushioning
Animation
Longitudinal slots ( )
allow the air ( ) to escape,
permitting dynamic, gentle movement into the end position
  26
Self-adjusting without adjusting screw
= Space-saving with no access required
= Quick commissioning
= Tamper-proof
…

## Slide 27: Accessories
Further use of accessories of the DSNU
Useful peripherals
SDBT-MSX
VFOE
PUN-H
VUVG-...-S

## Slide 28: Wide selection of accessories in the Core Range
Rod clevis
(SG)
Rod eye
(SGS)
Self-aligning rod coupler (FK)
Coupling piece (KSG)
Mounting component
(SMBR-8-)
Clevis foot (LBN)
Foot mounting
(HBN-S)
Tubing
e.g. PUN-H
Fitting and one-way flow control valve
e.g. VFOE
Proximity switch
e.g. SDBT-MSX
Proximity switch
e.g. SMT-8M-A
Core Range products Quickly available worldwide

## Slide 29: Engineering tools to ease your workload
DSNU-S
From the Festo Core Range - quickly available worldwide
 Simply order on the Online Portal
Quick access to CAD data
@PARTdataManager
Easy to select accessories
@Festo Design Tool FDT
PN 8155045
Pneumatic simulation
Simulation of the complete pneumatic chain

## Slide 30: Overview
 |  | Nominal size | Strokes | Cushioning | Magnet | Variants
Stays the same | DSNU (ISO) | Ø 12…40 | 10…320 mm (standard strokes) | P PPS from Ø 16 PPV from Ø 16 | Standard | None
 | DSNU (ISO) ESNU (ISO) | Ø 8…63 Production goods and goods for resale Ø 8/10/50/63 | 1…500 mm (longer on request) | P PPS from Ø 16 PPV from Ø 12 | Standard | X-strokes Modular kit (S2, S6, Q, R3, ATEX, etc.)
New | DSNU-S-... | Ø 8/12/16 Ø 20/25 | 10…200 mm (standard strokes) | P PPS from Ø 16 | Standard | None
 | DSNU-S-... | Ø 8…25 | 1…200 mm | P PPS from Ø 16 | Standard | X-strokes
DSNU (ISO), ESNU (ISO), DSNU-S-...



## Slide 31: Navigator
DSNU dimensions
DSNU-S dimensions
DSNU features
DSNU-S features
DSNU-S motivation
DSNU-S Interfaces
DSNU-S Sustainability
DSNU-S Application
Accessories
Features
Forces
Overview
PPS cushioning
Technical data